## Slide 1: Nao improvements for SPL
Tim Cooijmans, Tim Hendriks, Dionisio Nunes, Nico Petrakis, Marc Romeyn

## Slide 2: team
Dionisio Nunes
Marc Romeyn
Nico Petrakis
Tim Cooijmans
Tim Hendriks

## Slide 3: Robocup

## Slide 4: Robocup
Purpose
  Foster AI research
  Make AI appealing
  Brings many aspects of AI into light
Target
  Human like football skills by 2050!!!
  Awareness of challenges of robotics and AI
Means
  Standardized rules
  Multiples tools and platforms
  Competitions to check progress

## Slide 5: Overview
Vision
Aspects of vision
  Ball Detection (Marc)
  Goal Detection (Nico)
Kicking (Tim)
Locomotion
  Walking improvement (Tim C)

## Slide 6: Ball Detection
Goal:
  Solid ball detection without the need of calibration
Combining color detection and circle detection
  Color detection with loose color filters
    Detects lots of noise
  Use circle detection to find if output of color detection is ball or noise

## Slide 7: Color detection
Convert image from RGB to HSV
  Hue, Saturation and Value
Threshold the image
  See figure 1
Reduce noise
  See figure 2
  Blur
  Erode
Get the brightest pixel
Brightest pixel
Figure 1
Figure 2

## Slide 8: Circle detection
Convert input image to grayscale
  See figure 3
Canny edge detection
  See figure 4
Figure 3
Figure 4

## Slide 9: Circle detection
Smooth image
Detect circles in the image
  See figure 5
Ball found if there exists a circle with
  Radius between minimum and maximum radius of the ball
  Distance from center to output position of the color detection < radius
Next Nico on Goal Detection
Figure 5
.
Output from color detection

## Slide 10: Locating the goal
Found ball
In good position
Find goal
  Circle around the ball
Threshold pixels
Goal detection video
Next Tim H on Kicking

## Slide 11: Kicking
Kicking Video
Not balanced in every state
  No problem because of counter movement

## Slide 12: DEMO VIDEOS
Ball detection
Goal detection
Next on walking -Tim C

## Slide 13: Learning to walk
The learning problem
  Minimize expected distance to goal
  Based on observations from the past five (or so) timesteps
  By controlling joint positions and stiffnesses
High dimensionality
  The policy is a function from R^270 to R^38
  We will need
    Lots of data
    Dimensionality reduction
    A good initial policy

## Slide 14: Lots of data
Data collection method
  Repeatedly walk to uniformly random locations
  Observe sensory inputs and the actions chosen in response (at 50Hz)
  Lots of data in a very narrow region of state space
Inputs
  Accelerometer, gyroscope readings
  Joint positions and stiffnesses
  Goal location
Outputs
  Desired joint positions and stiffnesses

## Slide 15: A glance at the input data

## Slide 16: Output data

## Slide 17: Dimensionality reduction
Deep Auto-encoders (Hinton, 2006)
Based on Deep Belief Networks (Hinton, 2006)

## Slide 18: Deep features
From Honglak Lee et al. (2009)

## Slide 19: Deep Auto-encoders
From Hinton (2006)

## Slide 20: Putting it together

## Slide 21: The training procedure
Start with an initial policy π₀
Gather data with the policy
Pretrain the networks
Finetune by regression to find a new policy
Improve the policy by RL using the same data
Go to 2

## Slide 22: Expected difficulties
Deep belief nets are tedious to train
Limited control over the kind of features
  Fine-tuning may be too little, too late
Can't use NaoQI's inverse kinematics
  Which weren't that good to begin with
Reward function requires domain knowledge
  Simple functions may make poor learning signal
  Complex functions are likely buggy/noisy
  Next to conclude –Tim H

## Slide 23: conclusion
Ball and goal detection are not 100% accurate
Searching the ball takes too much time
Too less frames/sec to track rolling ball

## Slide 24: Future Research
State controller
Use both cameras
Goalkeeping
Parameterized kick
Locomotion
Communication between NAO’s

## Slide 25: Questions?